## Slide 1
Memory Interfacing

## Slide 2: Physical organization of memory and memory addressing
Each memory location can store one byte of data
The 8086 is a 16-bit microprocessor, it can transfer 16-bit data
This is stored by using 2 consecutive memory locations ,one for least significant byte and one for most significant byte

## Slide 3
To implement this entire memory is divided into 2 memory banks
The address space is physically connected to a 16-bit data bus by dividing the address space into two 8-bit banks of up to 512K bytes each
One bank is connected to the lower half of the 16-bit data bus (D0 – D7) and contains even address bytes. i.e., when A0 bit is low(0), the bank is selected. so it is referred as even addressed bank.

## Slide 4
The other bank is connected to the upper half of the data bus (D8 - D15) and contains odd address bytes. i.e., when A0 is high(1) and BHE (Bus High Enable) is low(0), the odd bank is selected. so it is referred as odd addressed bank.
A specific byte within each bank is selected by address lines A1-A19

## Slide 6
Data can be accessed from the memory in four different ways
8 - bit data from Lower (Even) address Bank
8 - bit data from Higher (Odd) address Bank
16 - bit data starting from Even Address
16 - bit data starting from Odd Address

## Slide 7: 8-bit data from Even address Bank

## Slide 8
To access memory bytes from Even address, information is transferred over the lower half of the data bus (D0 - D7)
The A0 is output LOW(0) and BHE is output HIGH(1) enabling only the even address bank

## Slide 9: 8-bit Data from Odd Address Bank

## Slide 10
To access memory byte from an odd address information, is transferred over the higher half of the data bus (D8 - D15)
The BHE output low(0) enables the upper memory bank(ODD)
A0 is output high(1) to disable the lower memory bank (EVEN)

## Slide 11: 16-bit Data Access starting from Even - Address

## Slide 12
16-bit data from an even address is accessed in a single bus cycle
Address lines A1 - A19 select the appropriate byte within each bank
A0 low and BHE low enables both banks simultaneously

## Slide 13: 16-bit Data Access starting from Odd Address

## Slide 14
A 16-bits word located at an odd address (two consecutive bytes with the least significant byte at an odd byte address) is accessed using two bus cycles
During the first bus cycle the lower byte (with the odd address 0005 as shown in fig. in previous slide) is accessed
During the second bus cycle, the upper byte (with the even address 0006H as in fig. in previous slide) is accessed

## Slide 15
During the first bus cycle, A1 - A19 address bus specifies the address and A0 is 1 and BHE is 0
Therefore the even memory bank is disabled and odd memory bank is enabled
During the second bus cycle, the address is incremented
Therefore A0 is 0 and BHE is made 1
The even memory bank is enabled and the odd memory bank is disabled

## Slide 16
Operation | BHE | A0 | Data Lines Used
Read/Write a byte at an even address | 1 | 0 | D7 – D0
Read/Write a byte at an odd address | 0 | 1 | D15 – D8
Read/Write a word at an even address | 0 | 0 | D15 – D0
Read/Write a word at an odd address | 0 1 | 1 0 | D15 – D8 in first operation byte from odd bank is transferred D7 – D0 in first operation byte from odd bank is transferred

## Slide 17
General procedure of static memory interfacing with 8086:
Arrange the available memory chips so as to obtain 16-bit data bus width.
  The upper 8 bit bank is called odd bank and lower 8 bit bank is called even bank
Connect available address lines of memory chips with those of the microprocessor
  Connect the memory RD and WR inputs to the corresponding processor control signals
  Connect 16 bit data bus with that of the microprocessor 8086

## Slide 18
The remaining address lines of the microprocessor, BHE and A0 are used for decoding the required chip select signals for the odd and even memory banks
  The CS of memory is derived from the O/P of the decoding circuit

## Slide 19: Interface 512KB RAM with 8086
Divide memory into odd/even address bank
Connect RD,WR of 8086 to RD,WR of RAM
If A0 is low(0), BHE is high(1) then Even bank is selected. That is data lines are D0-D7
If A0 is high(1),BHE is low(0) then Odd bank is selected. That is data lines are D8-D15

## Slide 20
8086 CPU has 20 address lines (00000h to FFFFFh)
RAM is of 512KB (1KB=1024 bytes=210 bytes)
Divide 512KB RAM into even and odd memory banks that is 512KB/2=256KB
Each bank is of 256KBytes
=256x210 bytes
=28x210bytes=218 bytes
18 address lines required to address memory location

## Slide 21: Address map…
Address | A19 | A18 | A17 | A16 | A15 | A14 | A13 | A12 | A11 | A10 | A9 | A8 | A7 | A6 | A5 | A4 | A3 | A2 | A1 | A0
80000h | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
RAM 1 AND 2 512KB: RAM1(256KB) RAM2(256KB) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
: : : |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
FFFFFh | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 22: Interfacing
8086 CPU
256KB RAM
(Odd Bank)
256KB RAM
(Even Bank)
A1-A18
A0-A17
A0-A17
RD
WR
RD
WR
RD
WR
CS1
CS2
D15-D8
D0-D7

## Slide 23: Memory Chip selection
C | BHE | A0 | CS1 | CS2
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 1
Input
Output
A19
C
BHE
A0
CS1
CS2
CS1=C + BHE
CS2=C + A0
C
ODD BANK
EVEN BANK
C = A19

## Slide 24: 80386DX and 80486(32-bit) Memory interface
80386DX and 80486 have 32-bit data buses and therefore 4 banks of memory
    32-bit, 16-bit and 8-bit transfers are accomplished by different combinations of the bank selection signals BE3, BE2, BE1, BE0.
    The Address bits A0 and A1 are used within the microprocessor to generate these signals

## Slide 25: Memory interface of 1GB RAM to 80386DX
80386DX CPU has 32 address lines: A0 to A31 (00000000h to FFFFFFFFh)
RAM is of 1GB (IGB=1024MB and IMB=1024 KB)
Divide 1GB RAM into 4 memory banks that is 1GB/4=256MB
Each bank is of 256KBytes
=256x210 X210 bytes
=28x210 X 210 bytes=228 bytes
28 address lines required to address memory location

## Slide 26: Address map…
Address: C0000000h to FFFFFFFFh
Address lines A0 to A27 of Memory are connected to address lines A2 to A29 of processor

## Slide 27: Interfacing
80386DX
256MB RAM
(BANK2)
256MB RAM
(BANK3)
256MB RAM
(BANK1)
256MB RAM
(BANK0)
A2-A29
A0-A27
A0-A27
A0-A27
A0-A27
E3
E1
E0
E2
D24-D31
D16-D23
D8-D15
D0-D7
BE0-BE3
A30-A31

## Slide 28: Memory Chip selection
A30
C
BE0
C
C = A30 . A31
A31
E0
BE1
C
E1
BE2
C
E2
BE3
C
E3
E1=C + BE1
E0=C + BE0
E2=C + BE2
E3=C + BE3

## Slide 29: 64 – bit processor memory interface
The Pentium, Pentium Pro, Pentium II and III contain a 64-bit data bus.
Therefore, 8 decoders or 8 write strobes are needed as well as 8 memory banks.
A0,A1 and A2 lines of processor are used for bank selection : BE7, BE6, BE5, BE4, BE3, BE2, BE1, BE0.

## Slide 30: Generation of Write Strobes
The write strobes are obtained by combining the bank enable signals (BEx) with the MWTC signal
MWTC(memory write command) is generated by combining the M/IO and W/R signals

## Slide 32: Memory interface of 512KB RAM to 64 bit processor(Pentium)
Pentium CPU has 32 address lines: A0 to A31 (00000000h to FFFFFFFFh)
RAM is of 512KB (IKB=1024B)
Divide 512KB RAM into 8 memory banks that is
512KB /8=64KB
Each bank is of 64KBytes
=64x210 bytes
=26x210 bytes=216 bytes
16 address lines required to address memory location

## Slide 33: Address map…
Address: FFF80000H – FFFFFFFFH
Address lines A0 to A15 of Memory are connected to address lines A3 to A18 of processor
A0,A1 and A2 lines of processor are used for bank selection : BE7, BE6, BE5, BE4, BE3, BE2, BE1, BE0.

## Slide 34: Pentium Memory Interface

## Slide 35
16L8 is a memory address decoder with 10 fixed inputs(I1 to I10) , two fixed outputs(O1,O8)
Address lines A19 to A31 are given as input to 16L8 decoder
U2 =A19….A28
CE= U2 A29 A30 A31

## Slide 36
The decoder output is given to memory bank enable signal(chip enable(CE))
OE(output enable) of all memory banks is connected to MRDC(memory read command)