## Slide 1: Modular Programming
Using procedures,
Using macros
Comparison between procedure and macro.

## Slide 2: Writing and using Procedures…
To avoid writing the sequence of instructions in the program each time you need them, you can write the sequence as a separate subprogram called a procedure
You use the CALL instruction to send the 8086 to the starting address of the procedure in memory

## Slide 3
A RET instruction at the end of the procedure returns execution to the next instruction in the main line
Procedures can even be nested

## Slide 4
MAINLINE OR CALLING
PROGRAM
NEXT MAINLINE
INSTRUCTIONS
PROCEDURE
INSTRUCTIONS
CALL
RET
Fig. Single Procedure Call

## Slide 5
Main Line Instructions
RET
Lower level
Procedure
CALL
RET
Procedure
CALL
Next Main Line
Instructions
Fig. Nested Procedures Call

## Slide 6: The CALL Instruction Overview
The 8086 CALL instruction performs 2 operations when it executes
First, it stores the address of the instruction after the CALL instruction on the stack
This address is called the return address because it is the address that execution will return to main program after the procedure executes

## Slide 7
If the CALL is to a procedure in the same code segment, then the call is near, and only the instruction pointer contents will be saved on the stack
If the CALL is to a procedure in another code segment, the call is far ; In this case both the instruction pointer and the code segment register contents will be saved on the stack

## Slide 8
Second operation of the CALL instruction is to change the contents of the instruction pointer and, in some cases, the contents of the code segment register to contain the starting address of the procedure

## Slide 9: The 8086 RET Instruction
A return at the end of the procedure copies the value from the stack back to the instruction pointer to return execution to the calling program
When the 8086 does a near call ,it saves the instruction pointer value for the instruction after the CALL on the stack
When the 8086 does a far call, it saves the contents of both the instruction pointer and the code segment register on the stack

## Slide 10
A RET instruction at the end of the procedure copies these values from the stack back into the IP and CS register to return execution to the mainline program

## Slide 11
The within segment form of RET copies a word from the top of the stack to the instruction pointer
The intersegment form of RET instruction is used to return from far procedures.
When this form of the Ret instruction executes, it will copy the word from the top of the stack to IP
Then it will increment the stack pointer by 2 and copy the next word from the stack to code segment register

## Slide 12: Writing and Calling near procedures…
CODE SEGMENT
ASSUME CS:CODE
:
:
CALL DELAY
:
MOV AH, 4CH
INT 21H
DELAY PROC NEAR
:
:
RET
ENDP
: ; define another procedure and so on
:
CODE ENDS
END START

## Slide 13
NOTE:
If the registers are modified in the procedure definition, programmer must push these registers onto the stack at the beginning of the procedure definition
Before executing the RET instruction, the register contents are restored back by popping off from stack

## Slide 14: Read 2 digit BCD and display using procedures…
data segment
bcd db ?
data ends
code segment
assume cs:code, ds:data
START:
MOV AX, DATA
MOV DS, AX
CALL READBCD
MOV bcd, AL
MOV BL, bcd
CALL DISPBCD
MOV AH, 4CH
INT 21H
READBCD PROC NEAR
MOV AH, 01H
INT 21H
MOV CL, 04
SHL AL, CL
MOV BL, AL
MOV AH, 01H
INT 21H
AND AL, 0FH
ADD AL, BL
RET
READBCD ENDP
DISPBCD PROC NEAR
MOV DL, BL
MOV CL, 04
SHR DL, CL
ADD DL, 30H
MOV AH, 02H
INT 21H
MOV DL, BL
AND DL, 0FH
ADD DL, 30H
MOV AH, 02H
INT 21H
RET
DISPBCD ENDP
CODE ENDS
END START

## Slide 15: Assignment…
Read 2 digit HEXA and display using procedures…

## Slide 16: Read 4 digit BCD(16 bits) and display using procedures…
DATA SEGMENT
bcd DW ?
DATA ENDS
CODE SEGMENT
ASSUME CS:CODE, DS:DATA
START:
MOV AX, DATA
MOV DS, AX
CALL READBCD
MOV AH, 00H
MOV bcd, AX
MOV CL, 08H
SHL bcd, CL
CALL READBCD
MOV AH, 00H
ADD bcd, AX
MOV BX, bcd
MOV BL, BH
CALL DISPBCD
MOV BX, bcd
;BL content to be displayed
CALL DISPBCD
MOV AH, 4CH
INT 21H

## Slide 17: Assignment…
Read 4 digit(16 bits) HEXA and display using procedures…
Linear Search/Binary Search – Read array elements and key to be searched from keyboard. Display the position where element is found.
Finding max/min in array – Read array elements from keyboard. Display the max/min number

## Slide 18: Passing parameters to and from procedures
When we call

## Slide 19: Writing and Using Assembler Macros…

## Slide 20: Assignment…
Compare Macro with Procedure

## Slide 21: Defining and Calling a Macro Without Parameters…
Macro Definition:
MACRO-NAME MACRO
; MACRO DEFINITION
;
ENDM
Invoking a Macro:
MACRO-NAME

## Slide 22: Example
Macro Definition:
CLRSCR MACRO
MOV AH, 00H
MOV AL, 02H
INT 10H
ENDM
Macro Invocation:
CLRSCR

## Slide 23: Passing Parameters to Macros
Example:
Macro definition:
SETCURSOR MACRO X, Y
MOV DL, Y
MOV DH, X
MOV BH, 00H
MOV AH, 02H
INT 10H
ENDM

## Slide 24
If the macro invocation statement is SETCURSOR 12, 40 then the macro will be replaced by:
MOV DL, 40
MOV DH, 12
MOV BH, 00H
MOV AH, 02H
INT 10H