## Slide 1: 8086 Assembler Directives
ASSUME,DB, DW, DD
END, ENDP, ENDS, EQU,
EVEN, EXTRN, GLOBAL
GROUP, INCLUDE, OFFSET
PROC, PUBLIC, SEGMENT, MACRO,

## Slide 2
Assembler Directives

## Slide 3
ASSUME
DB – Define Byte
DW – Define Word
DD – Define Double Word

## Slide 4
DQ – Define Quadword
Tell the assembler to declare a variable 4 words in length or to reserve 4 words of storage in memory
Example:
BIG_NUMBER DQ 243598740192A92BH

## Slide 5
DT – Define Ten Bytes
Tells the assembler to define a variable which is 10 bytes in length or to reserve 10 bytes of storage in memory
Example:
BIG_NUMBER DT 458733740192A92B8865H

## Slide 6
END – End Program
Last statement of a program to tell the assembler that this is the end of the program module
The assembler will ignore any statements after an END directive

## Slide 7
ENDP – End Procedure
This directive is used along with the name of the procedure to indicate the end of a procedure to the assembler

## Slide 8
ENDS – End Segment
This directive is used with the name of a segment to indicate the end of that logical segment

## Slide 9
EQU – Equate
Is used to give a name to some value or symbol
Each time the assembler finds the given name in the program, it will replace the name with the value or symbol you equated with that name

## Slide 10
EVEN – Align on Even Memory Address
The EVEN directive tells the assembler to increment the location counter to the next even address if it is not already at an even address
The 8086 can read a word from memory in one bus cycle if the word is at an even address

## Slide 11
If the word starts at an odd address, the 8086 must do two bus cycles to get the 2 bytes of the word
Therefore, a series of words can be read much more quickly if they are at even addresses
When EVEN is used in a data segment, the location counter will simply be incremented to the next even address
A NOP instruction will be inserted in the location incremented over

## Slide 12
Example:
DATA SEGMENT
A1 DB 9 DUP(?)
EVEN
; Increment Location counter to 000AH
B1 DW 100 DUP (0)
; Array of 100 words starting on even
address for quicker read
DATA ENDS

## Slide 13
EXTRN
The EXTRN directive is used to tell the assembler that the names or labels following the directive are in some other assembly module
The assembler will then put information in the object code file so that the linker can connect the two modules together

## Slide 14
GLOBAL – Declare Symbols as PUBLIC or EXTRN
The GLOBAL directive can be used in place of a PUBLIC directive or in place of an EXTRN directive
GLOBAL directive is used to make the symbol available to other modules

## Slide 15
GROUP – Group Related Segments
Is used to tell the assembler to group the logical segments named after the directive into one logical group segment
This allows the contents of all the segments to be accessed from the same group segment base

## Slide 16
Example:
SMALL_SYSTEM GROUP CODE, DATA, STACK_SEG
An appropriate ASSUME statement to follow this would be:
ASSUME CS:SMALL_SYSTEM, DS:SMALL_SYSTEM, SS:SMALL_SYSTEM

## Slide 17
INCLUDE – Include source code from file
Is used to tell the assembler to insert a block of source code from the named file into the current source module

## Slide 18
OFFSET
Tells the assembler to determine the offset or displacement of a named data item or procedure from the start of the segment which contains it
Example:
MOV SI, OFFSET PRICES

## Slide 19
ORG – Originate
The location counter is automatically set to 0000 when the assembler starts reading a segment
The ORG directive allows us to set the location counter to a desired value at any point in the program
The statement ORG 2000H tells the assembler to set the location counter to 2000H

## Slide 20
PROC – Procedure
Is used to identify the start of a procedure
The PROC directive follows a name you give the procedure

## Slide 21
PUBLIC
The PUBLIC directive is used to tell the assembler that a specified name or label will be accessed from other modules
Example:
PUBLIC A, B makes 2 variables A and B available to other assembly modules

## Slide 22
SEGMENT
Is used to indicate the start of a logical segment
Preceding the SEGMENT directive is the name you want to give the segment

## Slide 23
The statement, CODE SEGMENT for example, indicates to the assembler the start of a logical segment called CODE
The SEGMENT and ENDS directives are used to “bracket” a logical segment containing code or data

## Slide 24
Thank You…