## Slide 1: 8086 Instruction Set – 2
String instructions,
Flag control instructions,
Miscellaneous instructions.
Programs based on String instructions.

## Slide 2
String Instructions

## Slide 3: The 8086 String Instructions
Moving a String:
REPEAT
MOVE BYTE FROM SOURCE STRING
TO DESTINATION STRING
UNTIL ALL BYTES MOVED

## Slide 4
The more detailed algorithm is as follows:
INITIALIZE SOURCE POINTER, SI
INITIALIZE DESTINATION POINTER, DI
INITIALZE COUNTER, CX
REPEAT
COPY BYTE FROM SOURCE TO DESTINATION
INCREMENT SOURCE POINTER
INCREMENT DESTINATION POINTER
DECREMENT COUNTER
UNTIL COUNTER = 0

## Slide 5
The single 8086 string instruction MOVSB, will perform all the actions in the REPEAT-UNTIL loop
The MOVSB instruction will copy a byte from the location pointed to by the SI register to a location pointed to by DI register
It will then automatically increment/decrement SI and DI to point to the next source location

## Slide 6
If you add a special prefix called the repeat prefix ( REP ) in front of the MOVSB instruction, the MOVSB instruction will be repeated and CX decremented until CX is counted down to zero
In order for the MOVSB instruction to work correctly, the source index register, SI, must contain the offset of the start of the source string and the destination index register, DI, must contain the offset of the start of the destination location

## Slide 7
Also, the number of string elements to be moved must be loaded into the CX register
The string instructions will automatically increment or decrement the pointers after each operation, depending on the state of the direction flag DF

## Slide 8
If the direction flag is cleared with a CLD instruction, then the pointers in SI and DI will be automatically be incremented after each string operation
If the direction flag is set with an STD instruction, then the pointers in SI and DI will be automatically be decremented after each string operation

## Slide 9
Note:
For String instructions, an offset in DI is added to the segment base represented by the number in the ES register to produce a physical address
If DS and ES are initialized with the same value, then SI and DI will point to locations in the same segment

## Slide 10: Example…
DATA SEGMENT
TEST_MSG DB ‘HELLO’
NEW_LOC DB 5 DUP(0)
DATA ENDS
CODE SEGMENT
ASSUME CS:CODE, DS:DATA, ES:DATA
START: MOV AX, DATA
MOV DS, AX
MOV ES, AX

## Slide 11
LEA SI, TEST_MSG
LEA DI, NEW_LOC
MOV CX, 05
CLD
REP MOVSB
MOV AH, 4CH
INT 21H
CODE ENDS
END START

## Slide 12
Note:
The MOVSW instruction can be used to move a string of words; Depending on the state of the direction flag, SI and DI will automatically be incremented or decremented by 2 after each word move
If the REP prefix is used, CX will be decremented by 1 after each word move, so CX should be initialized with the number of words in the string

## Slide 13: Advantage of using MOVSB/MOVSW:
The string instruction is much more efficient than using a sequence of standard instructions, because the 8086 only has to fetch and decode the REP MOVSB instruction once
A standard instruction sequence such as MOV, MOV, INC, INC, LOOP etc would have to be fetched and decoded each time around the loop

## Slide 14: Using the CMPSB /CMPSW(Compare String Byte/WORD)
The CMPSB instruction will compare the byte pointed to by SI with the byte pointed to by DI and set the flags according to the result
It also increment/decrement the pointers SI and DI (depending on DF) to point to the next string elements

## Slide 15
The REPE prefix in front of this instruction tells the 8086 to decrement the CX register after each compare, and repeat the CMPSB instruction if the compared bytes were equal AND CX is not yet decremented down to zero
There are 2 conditions that will stop the repetition: CX=0 or string bytes or words not equal

## Slide 16: Example
DATA SEGMENT
STR1 DB ‘HELLO’
STR2 DB ‘HELLO’
DATA ENDS
CODE SEGMENT
ASSUME CS:CODE, DS:DATA, ES:DATA
START: MOV AX, DATA
MOV DS, AX
MOV ES, AX

## Slide 17
LEA SI, STR1
LEA DI, STR2
MOV CX, 05
CLD
REPE CMPSB
JNE NOTEQUAL
; DISPLAY EQUAL
JMP EXIT
NOTEQUAL:
; DISPLAY NOT EQUAL
EXIT: MOV AH, 4CH
INT 21H
CODE ENDS
END START

## Slide 18: SCASB, SCASW (Scan string byte, scan string word)
This instruction is the same as the earlier CMPSB, CMPSW instructions, except for the fact that the source for comparison is the register AL for SCASB, or AX for SCASW
The destination is the same, namely, ES:DI, and on execution, DI will point to the next byte or word, based on the instruction and the direction flag as in the earlier cases

## Slide 19
With CX initialized to the length of the destination array, and DI initialized to the array start address when D flag is reset, or to the end address of the array when the D flag is set, we can use the conditional instruction prefixes REPE (REPZ) or REPNE (REPNZ)
The repetition will then go on until the condition gets contradicted or until the register CX reaches zero (that is, the destination array is completed)

## Slide 20: Example:
;Scan a text string of 80 characters for a carriage return,0DH.
MOV DI,OFFSET TEXT_STRING
MOV AL,0DH
MOV CX,80
CLD
REPNE SCASB TEXT_STRING

## Slide 21: LODSB, LODSW: Load string byte into al, load string word into ax
These instructions are similar to MOVSB, MOVSW except the destination of the move becomes AL for LODSB, and AX for LODSW
The source is DS:SI
On execution the data will come to the register AL or AX, and SI will be properly modified
The REP or REPE (REPZ) prefix are like in the MOVES instructions

## Slide 22: Example
CLD
MOV SI,OFFSET SOURCE_STRING
LODSB

## Slide 23: STOSB, STOSW: Store string byte, store string word
Copies a byte from AL or a word from AX to a memory loc in ES pointed by DI
Similar to LODS, except the source is the accumulator, AL for byte store and AX for word store operations
The destination is ES:DI
The destination address modification after execution and repeat loop with CX initialized and using REP (REPE, REPZ) prefix will work like in LODS instructions

## Slide 24
This can be used to initialize a memory block with a fixed data as shown in the assembly language program segment below:
MOV CX, 100H
MOV DI, 500H
MOV AX, 0
REP STOSW
This program segment when executed will clear memory from address ES:500 to ES:6FF inclusive (100 words from address 500)

## Slide 25
Flag Control Instructions

## Slide 26: STC, CLC and CMC (Set Carry, Clear Carry and Complement Carry)
STC operation: CF ← 1;
CLC operation: CF ← 0;
CMC operation: CF ← NOT CF
No other flags are affected by these instructions

## Slide 27: STD and CLD (Set and Clear Direction Flag)
STD operation: DF ← 1; enables string addresses to be decremented
CLD operation: DF ← 0; enables string addresses to be incremented
Other flags are not affected by these instructions

## Slide 28: STI and CLI
These instructions modify the Interrupt control flag in the flag register
When this I flag is set, the processor is enabled to accept the hardware interrupts
Otherwise when it is reset, the processor will not be interrupted by activating the interrupt pin of the processor from the external hardware

## Slide 29
STI operation: IF ← 1; Hardware interrupts enabled
CLI operation: IF ← 0; Hardware interrupts disabled

## Slide 30: LAHF: Copy low byte of flag register to AH
Load flag register (lower byte) to register AH
This is flag register move instruction

## Slide 31: SAHF
Store the contents of AH register into the lower byte of Flag register
Loads the SF, ZF, AF, PF, and CF flags of the FLAGS register with values from the corresponding bits in the AH register (bits 7, 6, 4, 2, and 0, respectively)
Bits 1, 3, and 5 of register AH are ignored

## Slide 32: PUSHF and POPF
PUSHF pushes flag register onto stack
POPF pops top of the stack content into flag register

## Slide 33
Miscellaneous Instructions

## Slide 34: LEA (Load Effective Address)
This instruction computes the effective address of the second operand (the source operand) and stores it in the first operand (destination operand)
The source operand is a memory address (offset part) specified with one of the processors addressing modes; the destination operand is one of the 8 registers AX, BX, CX, DX, SI, DI, BP or SP

## Slide 35: NOP: No operation
This is a one byte instruction doing nothing except incrementing the IP by 1
It can also be coded in the assembly language as XCHG AX, AX, which also does nothing really
The machine code for XCHG AX, AX and NOP are the same; both are 90 H

## Slide 36: XLAT – Translate a Byte in AL
This instruction is used to translate a byte from one code to another code
The instruction replaces a byte in the AL register with a byte pointed to by BX in a lookup table in memory
Before the XLAT instruction can be executed, the lookup table containing the values for the new code must be put in memory and the offset of the starting address of the lookup table must be loaded in BX

## Slide 37
The code byte to be translated is put in AL
To point to the desired byte in the lookup table, the XLAT instruction adds the byte in AL to the offset of the start of the table in BX
It then copies the byte from the address pointed to by (BX+AL) back into AL
XLAT changes no flags

## Slide 38
Example:
; 8086 routine to convert ASCII code byte
; to EBCDIC(extended binary coded decimal interchange code) equivalent
; ASCII code byte is in AL at start
; EBCDIC code in AL at end
MOV BX, OFFSET EBCDIC_TABLE
;Point BX at start of EBCDIC table in DS
XLAT
; Replace ASCII in AL with EBCDIC from table